## Slide 1
Hands on analysis of conventional and advanced diffusion weighted MRI in the brain
Virendra R. Mishra, Ph.D.
Associate Professor, Department of Radiology
The University of Alabama at Birmingham
Sonal Krishan, M. D.
Associate Director, Body and GI Imaging
Medanta Hospital, India

## Slide 2
Hands on analysis of conventional and advanced diffusion weighted MRI in the brain body
Virendra R. Mishra, Ph.D.
Associate Professor, Department of Radiology
The University of Alabama at Birmingham
Sonal Krishnan, M. D.
Associate Director, Body and GI Imaging
Medanta Hospital, India

## Slide 3
Hao Huang, Ph.D. and other mentors at The University of Texas at Southwestern Medical Center (UTSW) at Dallas, TX.
Neurologists at the Cleveland Clinic Lou Ruvo Center for Brain Health, Las Vegas, NV
Neuroimaging Research Laboratory Members at the Cleveland Clinic Lou Ruvo Center for Brain Health, Las Vegas, NV
Neuroimaging Research Laboratory Members at the EN4D2 lab at the University of Alabama at Birmingham, Birmingham, AL; https://sites.uab.edu/en4d2/
Collaborators and Funding Acknowledgements (Mishra)
Research Participants
Mothers of the UTSW Developing Brains Cohort Study
Professional Fighters Brain Health Study
Funding Sources:
  NIH: Grant numbers P20GM109025 (PI: Cummings; Project-2 Leader: Mishra), R01NS117547 (PI: Mishra);
  Radiology Research Pilot Award (PI: Mishra);
  Philanthropy: Keep Memory Alive Young Scholar (PI: Mishra)

## Slide 4
Outline
Basics of Diffusion MRI
Artifacts and their corrected in preprocessing of dMRI
Groupwise analysis consideration
Advanced dMRI: DKI, NODDI, etc.…
dMRI outside the brain
Discussion

## Slide 5: dMRI is based on water diffusion measurement
In situ
2.5 – 3.0 x 10-3
mm2/s
0.6 - 0.8 x 10-3
mm2/s
Non-invasive

## Slide 6: Image Acquisition
6
RF
90
180
δ
Δ
G
Mori, 2007

## Slide 7
Outline
Basics of Diffusion MRI
Artifacts and their corrected in preprocessing of dMRI
Groupwise analysis consideration
Advanced dMRI: DKI, NODDI, etc.…
dMRI outside the brain
Discussion

## Slide 8
Problem # 1: Diffusion encoding gradients
8
Take home: DEC should be span the entire sphere in a non-planar and a non-collinear direction
You can check the directions of the acquisition using showdirs.m located at the GitHub page
Jones and Cercignani, 2010
(A)
(B)
(C)

## Slide 9
Problem # 2: Noise
9
Take home: Use dwidenoise in MrTrix located at https://www.mrtrix.org/; Steps also on GitHub page
Jones and Cercignani, 2010
-- Run Denoise: dwidenoise your_input_DWI.nii.gz your_denoised_DWI_output.nii.gz -noise your_noise_output.nii.gz -nthreads 96 -quiet -force
(A)
(B)

## Slide 10
Problem # 3: Susceptibility Artifacts
10
Take home: Always correct for these artifacts: See next slide on how to correct this in FSL
Jones and Cercignani, 2010
Using field map technique with two different echo times
Using reverse gradient method

## Slide 11
Problem # 4: Eddy current and Motion Artifacts
11
(A)
(B)
Conventional eddy-current correction
State of the art: eddy-current correction

## Slide 12
Problem # 4: Eddy current and Motion Artifacts
12
Take home: Always correct for these artifacts: FSL is currently the best. See GitHub document for the exact steps
-- Run Topup : topup –imain=your_denoised_data (AP/PA) –datain=acqparams.txt –config --config=b02b0.cnf --out=topup_results --iout=corr_b0 --fout=fieldmap --nthr=96
Acqparams.txt file:
0 1 0 0.1  Tells FSL that PA is the first volume
0 -1 0 0.1  Tells FSL that AP is the second volume
-- Run Eddy: eddy_cuda10.2 --imain=your_dwi_file --mask=skull_extracted_brain --acqp=acqparams.txt --index= row_of_1s_as_the_number_of_DEC --bvals=txt_file_with_b_values --bvecs=txt_file_with_bvecs --topup=topup_results --cnr_maps --residuals --estimate_move_by_susceptibility --mb=3 --mb_offs=1 --repol --out=desired_output_name -v
Tells FSL about the echo dwell time" multiplied by "number of PE steps - 1" and it is also the reciprocal of the PE bandwidth/pixel; Echo Spacing * EPI Factor - 1
Important points: You can also run topup and pass the results even if you don’t have opposite polarity data. Requirement is to have T1 and your DWI. You can download https://github.com/MASILab/Synb0-DISCO . Execution steps in GitHub

## Slide 13: Fit single tensors only at b-value<=1000s/mm2
13
b-value
(s/mm2)
500
1000
2000
3000
b-value
(s/mm2)
500
1000
2000
3000
~b>1500s/mm2
Take home: Only use b<=1000s/mm2 data if your acquisition has b-values>1000s/mm2. You can run dtifit in FSL to get your tensors. Exact execution steps in GitHub.

## Slide 14
Diffusion Tensor Imaging (DTI)
Diffusion ellipsoid
l1
l2
l3
Tensor Calculation
Measure diffusion along
various directions (> 6)
Diffusion ellipsoid
Positive symmetric
2nd order tensor
14

## Slide 15
Contrasts derived from Diffusion Tensor Imaging (DTI)
Axial Diffusivity
AxD = λ1
Radial Diffusivity
RD = λ2+ λ3
2
Mean Diffusivity
MD = λ1+ λ2+ λ3
3
DTI-based Tractography
15

## Slide 16
Outline
Basics of Diffusion MRI
Artifacts and their corrected in preprocessing of dMRI
Groupwise analysis consideration
Advanced dMRI: DKI, NODDI, etc.…
dMRI outside the brain
Discussion

## Slide 17
Run voxelwise statistics to answer your hypothesis
TBSS: Tract Based Spatial Statistics in FSL
Follow the steps outlined:
https://fsl.fmrib.ox.ac.uk/fsl/fslwiki/TBSS/UserGuide
TBSS uses intensity based registration which may not prove very sensitive to detecting differences
DTI-TK: Tensor Based Registration
Follow the steps outlined:
https://dti-tk.sourceforge.net/pmwiki/pmwiki.php?n=Documentation.HomePage and them run TBSS on this tensor registered file

## Slide 18
Atkinson-Clement et al., 2017
DTI changes in PD

## Slide 19
Mishra et al., 2019
DTI changes correlated with disease in PD

## Slide 20
Run nonparametric statistics in FSL
Either run randomise in FSL
randomise -i your_DWI_contrast -o your_desired_output_prefix -d design.mat -t design.con -m typically_your_denoised_eddy_corrected_brain_mask_derived_from_b0 -n 500 –T
2) You may also run palm in Matlab/Octave if you want to dig deeper into some complex analysis.
Execution steps in GitHub

## Slide 21
Outline
Basics of Diffusion MRI
Artifacts and their corrected in preprocessing of dMRI
Groupwise analysis consideration
Advanced dMRI: DKI, NODDI, etc.…
dMRI outside the brain
Discussion

## Slide 22
Additionally, brain voxels can contain cells or macromolecules
Gray Matter (GM) / CSF
GM and WM
Assaf et al, 2004
Isotropic
unrestricted
diffusion
Isotropic
restricted
diffusion
Anisotropic
Hindered
diffusion
Coherent WM

## Slide 23
Free-Water Corrected Diffusion Tensor Imaging (FW-DTI)
Free-water (fiso)
fiso-corrected AxD
fiso-corrected RD
fiso-corrected MD
fiso-corrected FA
Due to nonlinear fitting, at least 2 b-values dMRI data is required, both should be less than or equal to 1000s/mm2
You can run your eddy corrected dMRI data in DiPY: https://dipy.org/documentation/0.16.0./examples_built/reconst_fwdti/
Pasternak et al, 2009

## Slide 24
And there is intra-axonal water diffusion too!
Gray Matter (GM) / CSF
GM and WM
Isotropic
unrestricted
diffusion
Isotropic
restricted
diffusion
Anisotropic
Hindered and Restricted diffusion
WM
Assaf et al, 2004

## Slide 25
Diffusion Kurtosis Imaging (DKI)

## Slide 26
Diffusion Kurtosis Imaging (DKI)
Axonal Water
Fraction (AWF)
Axonal Kurtosis
(AK)
Radial Kurtosis
(RK)
Mean Kurtosis
(MK)
Due to nonlinear fitting, at least 2 b-values dMRI data is required, with one equal to 1000s/mm2 and one greater than or equal to 1500s/mm2
You can run DKI parameters on your eddy corrected dMRI using the code from NYU: https://github.com/jelleveraart/RobustDKIFitting
Jensen et al, 2005

## Slide 27
Neurite Orientation Dispersion and Density Imaging (NODDI)
ficvf
fiso
Orientation Dispersion
Index (ODI)
KAPPA
Zhang et al, 2012
Due to nonlinear fitting, at least 2 b-values dMRI data is required, with one equal to 1000s/mm2 and one greater than or equal to 1500s/mm2
You can run NODDI parameters on your eddy corrected dMRI using the Matlab code here: http://mig.cs.ucl.ac.uk/index.php?n=Download.NODDI

## Slide 28
Outline
Basics of Diffusion MRI
Artifacts and their corrected in preprocessing of dMRI
Groupwise analysis consideration
Advanced dMRI: DKI, NODDI, etc.…
dMRI outside the brain
Discussion

## Slide 29
Diffusion imaging in the breast
Donners et al, 2020

## Slide 30
Abdominal Diffusion Imaging
Donners et al, 2020

## Slide 31
Diffusion imaging in the pancreas
Donners et al, 2020

## Slide 32
Diffusion imaging in the kidneys
Donners et al, 2020

## Slide 33
Diffusion imaging in the kidneys
Donners et al, 2020

## Slide 34
Limited FOV diffusion imaging in the prostate
Donners et al, 2020

## Slide 35
Models routinely used for diffusion imaging outside the brain
Conventional single tensor model
2) Intravoxel incoherent motion (IVIM) model:
3) Diffusion Kurtosis Imaging
Le Bihan et al, 1986

## Slide 36
Outline
Basics of Diffusion MRI
Artifacts and their corrected in preprocessing of dMRI
Groupwise analysis consideration
Advanced dMRI: DKI, NODDI, etc.…
dMRI outside the brain
Discussion

## Slide 37
Discussions and Future Work
dMRI is a powerful technique to evaluate white matter disorganization in both neurodevelopment and neurodegenerative disorders.
Single tensor (ST)-dMRI metrics are very powerful and give us a good starting point to understand both white matter strength and brain configuration in neurological studies.
However ST-dMRI metrics are biased. Beyond ST-dMRI might provide additional insights into fiber dispersion, orientation, and inflammation through DKI and NODDI metrics.
Single tensor tractography is also biased in the crossing-fiber regions. Hence results derived from any tractographic techniques should be interpreted with caution.
Analysis of dMRI significantly affects the interpretation. Hence, a careful data processing is required.
Contact me